## Slide 1: D.1 Generators
Say we have an N = 100 turn, 10cm×10cm square loop,
rotating in a B = 2T magnetic field,
with frequency f = 60Hz rotating clockwise,
connected to an R = 200Ω lightbulb.
What is the maximum induced effective potential difference?
What’s the max induced current; which way past the lightbulb would it flow,
in the present orientation?
right
What max power is dissipated by the lightbulb?
v
The direction is easiest to
ascertain by considering where
FB = qv×B points on the front wire:

## Slide 2: D.1 Generators
Say we have an N = 100 turn, 10cm×10cm square loop,
rotating in a B = 2T magnetic field,
with frequency f = 60Hz rotating clockwise,
connected to an R = 200Ω lightbulb.
This power isn’t free.
While the magnetic field will generate a power-producing current,
Simultaneously, it’ll generate a power-sapping counter torque on the loop,
in effect, stealing power from you, to put power in the current.
What is the max torque? And what max power does the B-field steal?
i
FB
FB
So
So the powers are indeed equal/opposite.