## Slide 1
D.2 Motors
Say you want to lower a weight m = 50kg at 2.5m/s. So you connect a circuit,
where ξbat = ?, and its internal resistance is r = 200mΩ, and ℓ = 1.6m
and you immerse the circuit in a magnetic field B = 2T.
What should ξbat be? And which way should it point?
Now let’s see what current we need. So necessary force is:
Then let’s see what ξbat must be, using KVL…
First, the current must be pointed right along the bar to generate an upward FB = ℓI×B.
And this necessitates the battery to oriented + -.

## Slide 2: D.2 Motors
We got a battery w/ potential difference ξbat = ?, and internal resistance r = 50mΩ.
Connected to same 100 turn, 10cm×10cm loop.
And immersed in same B = 2T field.
Say we want to be able to raise a 20kg weight, about axle R = 5cm, at 2 rev/second.
What should ξbat be at least?
First let’s see what current we need. So necessary torque is:
Then let’s see how ξbat relates to this. Apply KVL to the loop…