## Slide 1
Simple Circuit
1. When connect light bulb to battery, can think of the battery as setting up an electric field (E, illustrated by blue lines) emanating from positive terminal, permeating the wires, and terminating on negative terminal. Note the field is not the same strength everywhere, but will in fact concentrate in the resistors.
5. At this point the electron is transported against the force of the battery’s ‘internal electric field’ by the battery’s internal chemical reactions.
e
3. This same process occurs through our lightbulb filament, but the energy transfer is greater, owing to the filament’s greater resistance, causing it to heat up so much as to begin to emit light.
2. All free electrons will be pushed through the wire by the field, gaining kinetic energy. But they will hit impurities in the wire, causing the e to transfer its kinetic energy to the wire, heating it up. This process occurs over and over again as the electron lurches along the wire, effectively drifting along a constant speed, called the drift velocity vd.
4. The electric field continues to cause the electron to lurch through the wire, and deliver energy to other devices in the same fashion as described in point 3, as it makes its way to the positive terminal.
6. And then the process repeats.

## Slide 2
Simple Circuit
Ec
1. The current through the circuit, I.
There are three quantities of interest to us in this process.
3. The rate at which energy is supplied by the battery, Pb, when it transports the electrons across its terminals.
2. The rate at which energy is used up (dissipated), PR, by (any) one of the resistors.
e

## Slide 3
Current
Ec
The current, I, through a device (resistor), is defined as the rate of flow of charge through that device. Or in other words, it’s the ratio of the amount of charge, Δq, that flowed through the device, to the amount of time, Δt, that it took.
First up is the current, I.
The units of current are:
What this will work out to be depends on two things:
1. The strength of the electric field in the resistor, or, from an equivalent perspective, the strength of the potential difference across it, ΔVR.
2. The resistance, R, of the resistor.
Each resistor may have its own distinct potential difference, and own distinct resistance, but the current through them must be the same, at least in the configuration below, by charge conservation!

## Slide 4
Current
Ec
Now we’d like to see how I, ΔVR, and R relate, as well as get an idea of what exactly R itself is, and how it can be calculated or measured.
e
E = ΔVR/L
e
e
e
e
e
v
To that end, let’s enlarge a section of our lightbulb resistor’s filament. We’ll take the section to have length L, and cross-section area A. The black circles are the impurities in the wire. Also depicting a typical filament electron being dragged through by the electric field, like a pinball through a pinball machine.

## Slide 5
Current
As a prelude to getting the current, let’s consider how this electron moves within the resistor. As mentioned, it will bounce around off impurities as it is slowly dragged along by the electric field.
It will generally accelerate against the direction of the field of course, but it will never pick up much speed because of the frequent collisions it makes with the impurities in the resistor.
So it will basically drift along at a constant rate (speed), vd.
Using a kinematics equation we can write this speed as:
average initial velocity after a collision is zero (because velocity is equally likely to point in any direction).
acceleration given by:
average time in between collisions
is called τ. This parameter must be looked up in table (or can calculate via other means).
So
Note high resistance materials will have a small τ, and low resistance materials will have a large τ.

## Slide 6
Current
Now that we have a formula for the drift speed of the electrons, we can get a formula for the current. Consider a bunch of electrons in a wire flowing right with drift velocity vd.
-
-
-
-
-
-
-
-
-
-
-
-
-
A short time Δt later, these electrons will have drifted right a distance vdΔt.
vd
And so the current would be:
E= ΔVR/L
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
d = vdΔt
The number of electrons that will have passed through our filament can be written as the product of two things:
So the number of electrons that will have passed through in this time is:
Amost there! So then the charge that will have passed through is:

## Slide 7
Ohm’s Law
And now we’re a short step away from Ohm’s law, which relates the current flowing through a resistor to the potential difference, ΔVR, across it:
This quantifies the ability of the resistor to impede electron flow, due to its intrinsic properties. It’s called the…
L/A quantifies the ability of the resistor to impede electron flow, due to its extrinsic properties (basically, its shape)
And the two combined, give the total resistance of the resistor:
And with that definition, we arrive at Ohm’s Law:
Also often written as:
We usually look ρ up in a table/online.

## Slide 8
Ohm’s Law
It’s worth while to pause and consider how the resistivity, ρ, varies with temperature and different types of material.
In a normal metal, like Copper, impurities provide mechanism for resistance, as described, even at low T’s. But as T increases, τ goes down (making ρ go up), because larger T causes the metal’s atoms to vibrate with greater and greater amplitude, causing them to more frequently collide with the electrons.
In a superconductor, the resistivity increases with T for the same reasons it does in a normal metal. But interestingly, when T gets low enough, τ  ∞, causing ρ  0. This happens because the electrons enter into a liquid-like state which prevents them from being scattered by impurities, or by oscillations of the superconductor’s atoms. Aluminum, for instance, superconducts, at T’s below 1.75K.
A semiconductor, like Silicon, is a cross between an insulator and and a conductor. Its main impediment to conduction is the fact that there are very few free electrons in it. But turns out, as T increases, this loosens up more free electrons (increasing n thereby) and so causing ρ to decrease. But eventually, the aforementioned atomic vibrations induced by higher T’s causes τ to become increasingly small, and make ρ start to increase again.

## Slide 9
Power Supplied and Used
Our main result is derived, but we had two more ancillary items on our list. We wanted to know how much power, Pb, is being supplied by the battery, and also how much power, PR, is being used up by the resistors (well, by any particular resistor).
Δq
So
Δq
If fill in Ohm’s Law result ΔVR = IR, then we can an equivalent (useful) formula:
So analogously

## Slide 10
Asside on how to calculate n
Might have noticed n (= # free electrons in sample per unit volume) shows up in our first formula for the current, and also in the resistivity. We often need to calculate this number, and here’s a way to do that…
Don’t forget to convert to kg!
And if you’d like to see how we got that…..

## Slide 11
Example
Suppose we hook a 100V battery up to a Germanium resistor via two (for the sake of discussion) resistanceless copper wires.
(a) What’s the resistance of the Ge resistor?
(b) What’s the current running through it?
(c) What’s the power delivered by the battery, and dissipated by the resistor?
We can use Ohm’s Law!
But what is ΔVR?
The wires are presumed approximately resistance-less (a good assumption), and will therefore have negligible potential difference across them. Therefore basically all the potential difference of the battery will be used up by the resistor. We’ll see how to relax this assumption later.
Or could say,
Of course in this circuit Pb must be equal to PR by energy conservation!

## Slide 12
Example
(d) What’s the drift speed of the electrons in the Ge resistor?
Remember I = nevdA.
And so their speed is:
(e) What’s the mean collision time in the Ge resistor?
So vd = I/neA.
We have I, e, and A, but we’ll need to get n.
FWIW, that’s only a hair’s width, every second.
This is τ, the number of seconds in between successive collisions for our hapless electron.
We can start with this formula, say:

## Slide 13
Example
(f) What’s the strength of the electric field in the in the Ge resistor?
Well, the strength of the electric field is given by: